## Slide 1: Trachs and Vents and CPT, Oh My!
Maple Landvoigt, MD
Pediatric Pulmonology
3/13/18

## Slide 2: Disclosures
I have no actual or potential conflict of interest in relation to this program/presentation.
I have no financial relationships to disclose.

## Slide 3: Objectives
Recognize children with special healthcare needs at risk for respiratory failure
Classify common reasons for and complications of tracheostomy
Describe the medical care of children with mechanical ventilators in school
Discuss common chronic illnesses in children that would benefit from airway clearance assistance
Review supplemental airway clearance techniques and devices

## Slide 4: The Technology Dependent Child

## Slide 5: Normal Airway Clearance
The body has 2 ways to move things out of the airway:
Cough
  Inspiration to expand the lungs
  Closure of the glottis and contraction of the respiratory muscles
  Expiration at high flow rates
Mucociliary escalator
  Microscopic hair like structures that “sweep” mucous up the lower airways
  Sensitive to airway fluid changes and “stickiness” of mucous

## Slide 6: Who is Prone to Impaired Airway Clearance?
Impairment of Cough Clearance:
Neurologic impairment (encephalopathy, Down Syndrome, muscular dystrophy)
Scoliosis or chest wall disorders
Floppy airways (tracheomalacia, bronchomalacia, bronchiectasis)
Tracheostomy
Impairment of Mucociliary Clearance:
Cystic fibrosis
Chronic aspiration
Tobacco smoke exposure

## Slide 7: Supplemental Airway Clearance
Activity – movement naturally increases airway clearance
Oral care/suctioning
Chest physiotherapy (CPT):
  Manual percussion
  Acapella device
  High Frequency Chest Wall Oscillation device – “Vest”
  Cough assist device
  Multiple other breath powered devices (flutter, PEP, etc)

## Slide 8: Oral Care and Suctioning
Positioning of patient with sialorrhea (excessive drooling)
  Children with severe and persistent sialorrhea may also benefit from medications to decrease secretions
Oral suctioning
  Health Care Procedure Manual for WV schools: S-99-101
Tracheostomy tube suctioning
  Health Care Procedure Manual for WV schools: S-123-126
  DO NOT pass suction catheter beyond the tip of the tracheostomy tube
  Catheter insertion depth can be matched to the length of the tube or specific physician order

## Slide 9: Manual Percussion Chest Physiotherapy
Postural drainage no longer recommended
Using a cupped hand to percuss the chest
May be used over the entire chest or focused on problem areas
Can also be performed using various “percussors”

## Slide 10: Acapella Device
Small, portable
Relatively inexpensive ($50)
Provides positive end expiratory pressure (PEEP) to “hold open” collapsible airways
Patient must be able to follow commands and breath out forcefully
https://www.youtube.com/watch?v=H6Rsdc7rjvA

## Slide 11: High Frequency Chest Wall Oscillation Device (Percussive Vest)
Passive
Well tolerated by most children
Expensive (~$16,000)
Somewhat portable

## Slide 12: Cough Assist Device
Can be used in cooperative or passive child
Takes practice for child and caregiver
Relatively expensive ($6-8,000)
Somewhat portable
Modality of choice for muscular dystrophy

## Slide 13: Cough Assist Use
Inspiratory pressure
  Typically start at +10 cmH2O for 0.5-1 sec for small children
  Work up to enough pressure to produce good chest rise (commonly +35-35 cmH2O)
Inspiratory pause/hold
  Initially may omit or should be as low as possible
Expiratory pressure
  Typically start at -10 cmH2O for 0.5-1 sec for small children
  Work up to opposite of inspiratory pressure (i.e. -35-45 cmH2O)
Breaths and cycles
  Standard treatment consists of 3-6 insp/exp breath “cycles” repeated 3-6 times

## Slide 14: Neuromuscular Weakness and Lower Airway Infections
Muscular dystrophy:
Frequently have swallowing dysfunction and aspiration
Impaired airway clearance due to respiratory muscle weakness
Hypoxic-ischemic encephalopathy:
Frequently have pooling of oral secretions (chronic aspiration)
Impaired airway clearance secondary to neuromuscular weakness/discoordination, often develop significant scoliosis
* Pneumonia is a leading cause of death in the neuromuscular population

## Slide 15: Non-Invasive Ventilation
Multiple interfaces positive pressure:
Full face
Nasal mask
Nasal pillows
Sip ventilation

## Slide 16: Invasive Ventilation
More common for children needing 24 hour ventilatory support
Requires a tracheostomy

## Slide 17: Home Ventilators
Common models:
Trilogy
LTV

## Slide 18: High Priority Ventilator Alarms
Circuit Disconnect
  Will occur when the tubing is disconnected
  Might occur with very large leak
  Check for disconnect, tracheostomy tube dislodged
High Pressure
  Can occur with mucous plugging
  Check patient for suctioning need, tracheostomy tube blockage
  Check circuit for kinks

## Slide 19: Common Reasons for Tracheostomy
Need for mechanical ventilation/Respiratory failure:
  Hypoventilation syndromes
  Bronchopulmonary Dysplasia
Unsafe or obstructed airway:
  Craniofacial anomalies
  Vocal cord lesions
  Subglottic stenosis
  Tracheal lesions
Neurologic abnormalities:
  Spinal cord/head trauma
  Hypoxic brain injury
Cyanotic heart disease or other surgical complications

## Slide 20: Routine Tracheostomy Care
Must be kept covered
  Speaking valve
  HME
  Capped
  Trach mask
Dressing changes, site care
Keeping ties tied
Suctioning

## Slide 21: Tracheostomy Complications
Common:
Granulation tissue (can bleed)
Site infections (candidiasis, staph, etc)
Leakage of secretions
Tracheal infections (MRSA, Pseudomonas, etc)
Mucous plugs
Impaired speech, swallowing
Emergent:
Large plugs (obstruction)
Dislocation (pulled out)
Bleeding into the airway

## Slide 22: Plan First!
All children with technology dependent lung disease attending school need a written care plan approved by parents, Primary Care Physician, Pulmonologist, school administration and nursing before enrollment. Plans should address:
All equipment needs
Level of staffing required
Staff training
Routine airway clearance (suctioning, chest physiotherapy, etc)
Routine sick regimen
Emergency procedures
Transportation safety
Parental concerns/anxiety

## Slide 23: Equipment Requirements
Recommended equipment for children with ventilators in school:
Primary ventilator (and back-up ventilator if indicated)
Extra battery
Heated humidifier
Extra tracheostomy tube(s)
Pulse oximeter
Portable suctioning equipment
Self-inflating bag and mask
Supplemental oxygen for emergency use
Airway clearance devices, nebulizer, or other equipment as indicated
From 2016 American Thoracic Society Home Ventilation Guidelines

## Slide 24: Required Staff Emergency Tracheostomy Skills
Verbalize criteria for calling emergency services
Be certified in CPR
Be able to contact parent and/or medical care team for urgent questions
Demonstrate use of self-inflating bag and mask in routine and emergency care procedures
List signs of tracheostomy obstruction
Demonstrate appropriate suctioning techniques to remove tracheostomy obstruction
Demonstrate an emergency tracheostomy tube change (change done by one staff member without assistance)
Demonstrate knowledge of emergency medications
Verbalize plans for loss of electricity, fire, tornado, or other natural disaster

## Slide 25: Required Ventilator Skills
Be able to assemble ventilator circuit and humidification system
Demonstrate how to properly turn the ventilator on and test the ventilator before use as well as view and verify settings
Verbalize that ventilator alarms must be audible throughout environment
Demonstrate an understanding of ventilator alarms and how to troubleshoot the alarms
Demonstrate the appropriate technique for draining tubing in the ventilator circuit (down and away from child)
Demonstrate the ability to add oxygen to circuit if indicated
Demonstrate how to connect and use the external battery for the ventilator
Verbalize understanding of the approximate battery life for each piece of equipment

## Slide 26: Children with Tracheostomies and/or on Home Ventilation are Special
Higher acuity, higher risk
Medical Home oversight should be provided by a collaborative partnership between the PCP and Pediatric Pulmonologist
  American Thoracic Society 2016
Require more intensive staffing (even 1:1)
High equipment burden
Transportation challenges
Cost

## Slide 27: WV Pediatric Pulmonology Providers
Maple Landvoigt, MD
  WVU (Morgantown):
  Pediatric Pulmonology Nurse: 304-598-6055
  Emergencies/Physician call line 304-598-6000, ask for me to be paged
  WVSOM/Robert C Byrd Clinic (Lewisburg):
  Pediatric Nurse: 304-645-3220 ext 1287
  After hours: 304-645-3220, ask for me to be paged
Kevin Maupin, MD
  CAMC/Women’s and Children’s:
  304-388-5432

## Slide 28: The End